Spreadsheet Computations and Dependencies

Columns in sheet:
- Frame #
- Event Comments
- Time (seconds)
- Miles per Hour (MPH, described as “s” or speed in formulas)
- Feet per Second (FPS, described as “v” or velocity in formulas)
- Acceleration or Deceleration Indicator
- Factor (described as a “f” variable in formulas)
- Percent (% of completion of each vehicles event)
- Incrimental distance
- Total distance (sum of Incrimental Distance)

*The last 7 columns repeat for each additional vehicle. *

Known Factors (variables) that are previously gathered and inputed by the user:
- Vehicle Name or Description
- Original Speed (prior to skidmarks, MPH)
- Drag Factor (described as a “f” variable in formulas)
- Acceleration or Deceleration
- Pre-Crash Time (seconds)
- Impact Speed (MPH)
- Acceleration or Deceleration
- Speed Immediately After Impact (not a required entry, MPH)
- Speed when Vehicles Seperate (MPH)
- Crash Impulse (time elapsed from Impact speed to Vehicles Seperate, seconds, typically .1 to .2 seconds)
- Post Crash Drag Factor
- Acceleration or Deceleration

Specific Behavoirs needed:
- All decimal places kept whole. Rounding is not preferred.
- Report 4 decimal places in each cell (truncated)
- Frames are 0.0333333333 seconds apart
  - Exceptions are for the Pre-Crash time
  - That time needs to be properly inserted when the Impact speed is reached
  - That time should be used as an incremental point for all vehicles
  - The time immediately after this time should carry on the cadence of 0.0333333333
    - Such as Row 1: 0.0333333333, Row 2: 0.045, Row 3: 0.06666666666, Row 4: 0.099999
- FPS calculated
  - from “Original Speed” to “Impact Speed”.
  - Insert Impact Speed when calculation drops just below the “Impact Speed”
  - continue calculation until reaching “Speed at Seperation”
  - Insert the “Speed at Seperation” and continue until reaching 0 MPH.
  - Formula needs to convert the imputed MPH for Comparision or we have to require the FPS to be entered and not MPH
- Factor
  - Inputed for Pre-Crash and Post Crash
  - Calculated for intervals between Speed after impact to Seperation
  - It would be great if it could be fine tuned later, but I can see that being difficult
    - The factor changes as a vehicle slides, rolls, etc across multiple surfaces
- MPH
  - Calculated off FPS = FPS/1.466666666666666
- Lining up crashes
  - In a 2 vehicle crash they crash at the same time.
  - With 3 or more vehicles the impact time will be at different times.
  - It is not likely they would all collide at the exact same moment
  - Most calculations will be only 2 vehicles.

Formulas:

Time
0.0333333333 + previous time
Exceptions is when reaching Impact Speed, use Impact Time then return to same frames ie: for the frame after the Impact time
Time Previous to Impact Time + 0.0333333333333

MPH
S=V over 1.4666666666

FPS
Deceleration
V sub f=V sub o-(32.2*f*t)

Acceleration
V sub f=V sub o+(32.2*f*t)

Factor (for speed after impact to seperation)
Deceleration
f=(V sub o- V sub f)over(32.2 * t)

Acceleration

f=(V sub f- V sub o)over(32.2 * t)

Percent
Different for each vehicle.
Percent =(Current Time) over (End Time)

Incremental Distance
d=16.1 * f* t sup 2

Variables:

d = distance
f = Acceleration/Deceleration Factor
t = time (seconds)
v = velocity (feet per second)
s = speed (MPH)
Vo = Velocity Original
Vf = Velocity Final